## Slide 1: Chapter 1
Computer Abstractions and Technology
Lesson 3: More on Performance

## Slide 2: Today
More on Performance
Power Trend
Integrated Technology
Amdhal’s Law
MIPS … and MIPS!
Remember: HW1 has been already issued!

## Slide 3: Review
Performance = 1/Execution Time
Response time - How long it takes to do a task (it includes disk access, memory access, I/O activities, operating systems overhead, etc)
  Aka …. execution time, or elapsed time
Throughput - Total work done per unit time
  (aka bandwidth)
CPU time - the time spent by the CPU to complete his task (doesn't include I/O or time spent running other program)
  system CPU time - time spent in OS tasks on behalf of a program;
  user CPU time (also called CPU performance or CPU execution time) - time spent by the CPU in a program itself

## Slide 4: Review (cont.)
Clock cycles - the discrete time interval in which events take place in the hardware
  Aka tick, clock tick, clock, cycles
  Clock period = length of a clock cycle
Clock frequency - number of cycles per second
  aka clock rate
  measured in Hertz

## Slide 5: CPI Example
Computer A: ClockCycle Time = 250ps, CPI = 2.0
Computer B: ClockCycle Time = 500ps, CPI = 1.2
  Same ISA (Instruction Set Architecture)
Which is faster, and by how much?
A is …
…1.2 times as fast as B

## Slide 6: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency

## Slide 7: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc
The BIG Picture

## Slide 8: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5
Sequence 2 is faster even though it uses more instructions

## Slide 9: Power Trends
In CMOS Integrated Circuit (IC) technology
  CMOS (Complementary Metal Oxide Semiconductor)
§1.5 The Power Wall
×1000
×30
5V → 1V

## Slide 10: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 11: Uniprocessor Performance
§1.8 The Sea Change: The Switch to Multiprocessors
Constrained by power, instruction-level parallelism, memory latency

## Slide 12: Multiprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization

## Slide 13: Manufacturing ICs
Yield: proportion of working dies per wafer

## Slide 14: Intel Core i7 Wafer
300mm wafer, 280 chips, 32nm technology
Each chip is 20.7 x 10.5 mm

## Slide 15: Integrated Circuit Cost
Nonlinear relation to area and defect rate
  Wafer cost and area are fixed
  Defect rate determined by manufacturing process
  Die area determined by architecture and circuit design

## Slide 16: Concluding Remarks
Cost/performance is improving
  Due to underlying technology development
Hierarchical layers of abstraction
  In both hardware and software
Instruction set architecture
  The hardware/software interface
Execution time: the best performance measure
Power is a limiting factor
  Use parallelism to improve performance
§1.9 Concluding Remarks

## Slide 17: Improving Performance - Amdahl’s Law
Pitfall: Improving an aspect of a computer and expecting a proportional improvement in overall performance
§1.10 Fallacies and Pitfalls
Example:
"Suppose a program runs in 100 seconds on a machine, with multiply responsible for 80 seconds of this time.
How much do we have to improve the speed of multiplication if we want the program to run 4 times faster?“

## Slide 18: Amdahl's Law
How about making it 5 times faster?
20sec = 20sec + (80sec / n) impossible!!!!
Principle: Make the common case fast
To be 4 times faster the program should run in 100/4 seconds (i.e. 25 seconds)
25s = (80s / n) + 20s  n = 80/5 = 16s
  i.e. the multiplication should run in 16 seconds.

## Slide 19: Remember
Performance is specific to a particular program/s
  Total execution time is a consistent summary of performance
For a given architecture performance increases come from:
  increases in clock rate (without adverse CPI affects)
  improvements in processor organization that lower CPI
  compiler enhancements that lower CPI and/or instruction count
  Algorithm/Language choices that affect instruction count
Pitfall: expecting improvement in one aspect of a machine’s performance to affect the total performance

## Slide 20: Pitfall: MIPS as a Performance Metric
MIPS: Millions of Instructions Per Second
  Doesn’t account for
    Differences in ISAs between computers
    Differences in complexity between instructions
  CPI varies between programs on a given CPU

## Slide 21: Next Lecture and Reminders
Next lecture
  MIPS NOT as millions of Instructions per second
  MIPS-32 and 64 instruction Set
    Reading assignment – PH, The entire Chapter 1
Reminders
  HW1 has been assigned and it due this week
  HW2 will be show up on Thursday