## Slide 1: Chapter 1
Computer Abstractions and Technology
Lesson 2: Understanding Performance

## Slide 2
Indeed, the cost-performance ratio of the product will depend most heavily on the implementer, just as ease of use depends most heavily on the architect.
The Mythical Man-Month, Brooks, pg 46

## Slide 3: So far…
Progress in computer technology has been revolutionary
The Computer Components
  I/O
    Mouse, Monitor,
    Printer, etc.
  Processor
  Memory
    Volatile main memory
    Non Volatile secondary
    memory

## Slide 4: Performance Metrics
Purchasing perspective
  given a collection of machines, which has the
    best performance?
    least cost?
    best cost/performance?
Design perspective
  faced with design options, which has the
    best performance improvement?
    least cost?
    best cost/performance?
Both require
  basis for comparison
  metric for evaluation
Our goal is to understand what factors in the architecture contribute to overall system performance and the relative importance (and cost) of these factors
Notes: Or smallest/lightest
Longest battery life
Most reliable/durable (in space)

## Slide 5: Technology Trends
Electronics technology continues to evolve
  Increased capacity and performance
  Reduced cost
Year | Technology | Relative performance/cost | 
1951 | Vacuum tube | 1 | 
1965 | Transistor | 35 | 
1975 | Integrated circuit (IC) | 900 | 
1995 | Very large scale IC (VLSI) | 2,400,000 | 
2013 | Ultra large scale IC | 250,000,000,000 | 
DRAM capacity
§1.5 Technologies for Building Processors and Memory

## Slide 6: Defining Performance
Which airplane has the best performance?
§1.4 Performance

## Slide 7: Response Time
Response time How long it takes to do a task
  The length includes disk access, memory access, I/O activities, operating systems overhead, etc.
  Important to individual users but often not good for comparison purposes
  Good to determine system performance
It is also called execution time, or elapsed time

## Slide 8: Response Time and Throughput
Throughput (also called bandwidth)
  Total work done per unit time
    e.g., tasks/transactions/… per hour
    Important to data center managers
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
We’ll focus on response time for now…

## Slide 9: Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
Example: time taken to run a program 10s on A, 15s on B. How much faster is A than B?
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B
Notes: Increasing performance requires decreasing execution time

## Slide 10: Another Example
Problem:
  machine A runs a program in 20 seconds
  machine B runs the same program in 25 seconds
Question: How much faster is A than B?
The performance ratio is:
  25/20 = 1.25
  i.e. A is 1.25 faster than B
  If A is n times faster than B, then
performanceA execution_timeB
-------------------- = --------------------- = n
performanceB execution_timeA
Notes: Increasing performance requires decreasing execution time

## Slide 11: Measuring Execution Time
CPU time
  the time spent by the CPU to complete his task and doesn't include I/O or time spent running other program
  it includes user CPU time and system CPU time
    system CPU time - time spent in OS performing tasks on behalf of a program;
    user CPU time (also called CPU performance) - time spent by the CPU in a program itself
  Different programs are affected differently by CPU and system performance
    CPU performance refers to the user CPU time
      aka CPU execution time

## Slide 12: Metric Units
The principal metric prefixes.

## Slide 13: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock (cycles)
Data transfer and computation
Update state
Clock period
Clock cycles, also called tick, clock tick, clock, cycles = the discrete time interval in which events take place in the hardware

## Slide 14: Definitions and Formulas
Clock period = length of a clock cycle
  measured in time units
    e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency, also called clock rate = number of cycles per second
  measured in Hertz
    1 Hz = 1 cycles/sec
    kHz (kilohertz, 103 Hz), MHz (megahertz, 106 Hz), GHz (gigahertz, 109 Hz) and THz (terahertz, 1012 Hz)
      e.g., 4.0GHz = 4000MHz = 4.0×109Hz

## Slide 15: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade-off clock rate against cycle count
CPU execution Time per program, in brief CPU Time
per program

## Slide 16: CPU Time Example
Computer A has a 2GHz clock. Program P runs in 10s (i.e. takes 10s of CPU time)
We want to design computer B
  We aim to run P in 6s of CPU time
  We make a faster clock (increase the clock rate) which causes an increase of 1.2 × clock cycles for P on B with respect to (wrt) A
How fast must computer B clock be? (i.e. what is B’s clock rate?)

## Slide 17: Performance
A program is made of instructions. The more instructions, the longer is the time required to execute the program.
Each instruction takes a certain amount of time
  Some take several clock cycles (take longer time) some take just a few cycles (take a shorter time)
  Let us consider an average time per instruction (average clock Cycles Per Instruction)
A formula that expresses the execution time in terms of the instruction number consider multiplying the number of instructions (Instruction Count) for the average time used by an instruction (average clock CPI)

## Slide 18: Instruction Count (IC) and Cycles Per Instruction (CPI)
Instruction Count for a program (IC)
  Determined by the program, the ISA and the compiler
Average cycles per instruction (CPI)
  Determined by the CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 19: Next Time
More on Performance
Power Trend
Integrated Technology
Amdhal’s Law
MIPS
HW 1 is issued