## Slide 1: Chapter 2
Computer Abstractions and Technology
Lesson 4: Instructions - Language of the Computer

## Slide 2: Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets
§2.1 Introduction

## Slide 3: The MIPS Instruction Set
Used as the example throughout the book
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
  See MIPS Reference Data tear-out card, and Appendixes B and E

## Slide 4: MIPS (RISC) Design Principles
Simplicity favors regularity
  fixed size instructions – 32-bits
  small number of instruction formats
  opcode always the first 6 bits
Good design demands good compromises
  three instruction formats
Smaller is faster
  limited instruction set
  limited number of registers in register file
  limited number of addressing modes
Make the common case fast
  arithmetic operands from the register file (load-store machine)
  allow instructions to contain immediate operands

## Slide 5: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favours regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware

## Slide 6: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1

## Slide 7: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations
§2.3 Operands of the Computer Hardware

## Slide 8: Aside: MIPS Register Convention
Name | Register Number | Usage | Preserve on call?
$zero | 0 | constant 0 (hardware) | n.a.
$at | 1 | reserved for assembler | n.a.
$v0 - $v1 | 2-3 | returned values | no
$a0 - $a3 | 4-7 | arguments | no
$t0 - $t7 | 8-15 | temporaries | no
$s0 - $s7 | 16-23 | saved values | yes
$t8 - $t9 | 24-25 | temporaries | no
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return addr (hardware) | yes
$k0-$k1 | 26-27 | reserved for the OS kernel | no

## Slide 9: MIPS Arithmetic Instructions
MIPS assembly language arithmetic statement
add $t0, $s1, $s2
sub $t0, $s1, $s2
Each arithmetic instruction performs only one operation
Each arithmetic instruction fits in 32 bits and specifies exactly three operands
  destination  source1 op source2
Those operands are all contained in the datapath’s register file ($t0,$s1,$s2) – indicated by $
Operand order is fixed (destination first)
Notes: For class handout

## Slide 10: MIPS Arithmetic Instructions
MIPS assembly language arithmetic statement
add $t0, $s1, $s2
sub $t0, $s1, $s2
Each arithmetic instruction performs only one operation
Each arithmetic instruction fits in 32 bits and specifies exactly three operands
  destination  source1 op source2
Each arithmetic instruction performs only one operation
Each arithmetic instruction fits in 32 bits and specifies exactly three operands
  destination  source1 op source2
Operand order is fixed (destination first)
Those operands are all contained in the datapath’s register file ($t0,$s1,$s2) – indicated by $
Notes: For lecture

## Slide 11: MIPS R3000 Instruction Set Architecture (ISA)
Instruction Categories
  Computational
  Load/Store
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
Registers
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
3 Instruction Formats: all 32 bits wide
R format
I format
J format

## Slide 12: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1

## Slide 13: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4
MIPS is Big Endian
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address

## Slide 14: Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register

## Slide 15: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word

## Slide 16: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 17: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
  addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction

## Slide 18: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add $t2, $s1, $zero

## Slide 19: Review: Unsigned Binary Representation
Hex | Binary | Decimal
0x00000000 | 0…0000 | 0
0x00000001 | 0…0001 | 1
0x00000002 | 0…0010 | 2
0x00000003 | 0…0011 | 3
0x00000004 | 0…0100 | 4
0x00000005 | 0…0101 | 5
0x00000006 | 0…0110 | 6
0x00000007 | 0…0111 | 7
0x00000008 | 0…1000 | 8
0x00000009 | 0…1001 | 9
 | … | 
0xFFFFFFFC | 1…1100 | 
0xFFFFFFFD | 1…1101 | 
0xFFFFFFFE | 1…1110 | 
0xFFFFFFFF | 1…1111 | 
232 - 1
232 - 2
232 - 3
232 - 4
232 - 1
1 1 1 . . . 1 1 1 1 bit
31 30 29 . . . 3 2 1 0 bit position
231 230 229 . . . 23 22 21 20 bit weight
1 0 0 0 . . . 0 0 0 0 - 1
Notes: All positive numbers - no sign bit
last entry is most significant byte address
fourth from last entry is most significant word address

## Slide 20: Aside: Beyond Numbers
American Std Code for Info Interchange (ASCII): 8-bit bytes representing characters
ASCII | Char |  | ASCII | Char | ASCII | Char | ASCII | Char |  | ASCII | Char | ASCII | Char
0 | Null |  | 32 | space | 48 | 0 | 64 | @ |  | 96 | ` | 112 | p
1 |  |  | 33 | ! | 49 | 1 | 65 | A |  | 97 | a | 113 | q
2 |  |  | 34 | “ | 50 | 2 | 66 | B |  | 98 | b | 114 | r
3 |  |  | 35 | # | 51 | 3 | 67 | C |  | 99 | c | 115 | s
4 | EOT |  | 36 | $ | 52 | 4 | 68 | D |  | 100 | d | 116 | t
5 |  |  | 37 | % | 53 | 5 | 69 | E |  | 101 | e | 117 | u
6 | ACK |  | 38 | & | 54 | 6 | 70 | F |  | 102 | f | 118 | v
7 |  |  | 39 | ‘ | 55 | 7 | 71 | G |  | 103 | g | 119 | w
8 | bksp |  | 40 | ( | 56 | 8 | 72 | H |  | 104 | h | 120 | x
9 | tab |  | 41 | ) | 57 | 9 | 73 | I |  | 105 | i | 121 | y
10 | LF |  | 42 | * | 58 | : | 74 | J |  | 106 | j | 122 | z
11 |  |  | 43 | + | 59 | ; | 75 | K |  | 107 | k | 123 | {
12 | FF |  | 44 | , | 60 | < | 76 | L |  | 108 | l | 124 | ¦
15 |  |  | 47 | / | 63 | ? | 79 | O |  | 111 | o | 127 | DEL
Notes: see Figure 3.15 in the book for the complete listing - note that we are only using 7 of the 8 bits (7 bits gives us 127 encodings) - the extra bit can be used as a parity bit to detect single bit errors during transmission
Note that upper and lower case letters differ by exactly 32
13 is carriage return
0 is Null (marking the end of string in C)

## Slide 21: Unsigned Binary Integers
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295
§2.4 Signed and Unsigned Numbers

## Slide 22: 2s-Complement Signed Integers
Given an n-bit number
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 1111 1111 1111 1111 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
Using 32 bits
  –2,147,483,648 to +2,147,483,647

## Slide 23: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 24: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 00102
  –2 = 1111 1111 … 11012 + 1 = 1111 1111 … 11102

## Slide 25: Sign Extension
Representing a number using more bits
  Preserve the numeric value
In MIPS instruction set
  addi: extend immediate value
  lb, lh: extend loaded byte/halfword
  beq, bne: extend the displacement
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110

## Slide 26: Representing Instructions
Instructions are encoded in binary
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
Register numbers
  $t0 – $t7 are reg’s 8 – 15
  $t8 – $t9 are reg’s 24 – 25
  $s0 – $s7 are reg’s 16 – 23
§2.5 Representing Instructions in the Computer

## Slide 27: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 28: R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 29: Conclusion
  MIPS as millions of Instructions per second (do not confuse with the MIPS language!)
  Amdhal’s Law
  MIPS-32 and 64 Instruction Set
    Reading assignment – PH, Chapter 2
Next time…we continue Ch 2