## Slide 1: Chapter 3
Computer Abstractions and Technology
Lesson 6: Arithmetic for Computers

## Slide 2: Arithmetic for Computers
Arithmetic for Computers
  Addition
  Subtraction
  Multiplication
Today’s Lecture
  Chap 3, 3.1-3.3
  Appendix C – Review Logic and Circuits

## Slide 3: Review: MIPS Organization
Processor
Memory
32 bits
230
words
read/write
addr
read data
write data
word address
(binary)
0…0000
0…0100
0…1000
0…1100
1…1100
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
registers
($zero - $ra)
32
32
32
32
32
32
5
5
5
PC
ALU
32
32
32
32
32
0
1
2
3
7
6
5
4
byte address
(big Endian)
Fetch
PC = PC+4
Decode
Exec
Add
32
32
4
Add
32
32
branch offset

## Slide 4: Review: MIPS Addressing Modes
1. Operand: Register addressing
op rs rt rd funct
Register
word operand
op rs rt offset
2. Operand: Base addressing
base register
Memory
word or byte operand
3. Operand: Immediate addressing
op rs rt operand
4. Instruction: PC-relative addressing
op rs rt offset
Program Counter (PC)
Memory
branch destination instruction
5. Instruction: Pseudo-direct addressing
op jump address
Program Counter (PC)
Memory
jump destination instruction
||

## Slide 5: MIPS Number Representations
32-bit signed numbers (2’s complement): 0000 0000 0000 0000 0000 0000 0000 0000two = 0ten 0000 0000 0000 0000 0000 0000 0000 0001two = + 1ten ...
0111 1111 1111 1111 1111 1111 1111 1110two = + 2,147,483,646ten 0111 1111 1111 1111 1111 1111 1111 1111two = + 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0000two = – 2,147,483,648ten 1000 0000 0000 0000 0000 0000 0000 0001two = – 2,147,483,647ten ...
1111 1111 1111 1111 1111 1111 1111 1110two = – 2ten 1111 1111 1111 1111 1111 1111 1111 1111two = – 1ten
maxint
minint
MSB
LSB

## Slide 6: Review: 2’s Complement Binary Representation
2’sc binary | decimal
1000 | -8
1001 | -7
1010 | -6
1011 | -5
1100 | -4
1101 | -3
1110 | -2
1111 | -1
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
23 - 1 =
-(23 - 1) =
-23 =
1010
complement all the bits
1011
and add a 1
Note: negate and invert are different!
Assume n=3
  n is the no. of bits
Negate
Notes: Signed numbers – assuming 2’s complement representation – for eight bits
Note that msb of 1 indicates a negative number, the bit string all 0’s is zero, that the largest positive number that can be represented is 7 (2**(n-1) –1 for n bits) whereas the largest negative number that can be represented is –8 (-2**(n-1) for n bits)

## Slide 7: MIPS Sign Extend
In byte or half word, the sign extension repeats the most significant bit until the whole word is filled.
Converting <32-bit values into 32-bit values
  copy the most significant bit (the sign bit) into the “empty” bits 0010 -> 0000 0010 1010 -> 1111 1010
sign extend versus zero extend
    i.e. add versus addu

## Slide 8: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
Floating-point real numbers
  Representation and operations
§3.1 Introduction

## Slide 9: MIPS Arithmetic Logic Unit (ALU)
Must support the Arithmetic/Logic operations of the ISA
  add, addi, addiu, addu
  sub, subu, neg
  mult, multu, div, divu
  sqrt
  and, andi, nor, or, ori, xor, xori
  beq, bne, slt, slti, sltiu, sltu
32
32
32
m (operation)
result
A
B
ALU
4
zero
ovf
1
1
With special handling for
  sign extend – addi, addiu andi, ori, xori, slti, sltiu
  zero extend – lbu, addiu, sltiu
  no overflow detected – addu, addiu, subu, multu, divu, sltiu, sltu

## Slide 10: Integer Addition and Subtraction
Example: 7 + 6
Subtraction is an the addition of the negation of the second operand
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
§3.2 Addition and Subtraction

## Slide 11: Examples of Overflow Detection
Overflow: the result is too large to represent in 32 bits
Overflow occurs when
  adding two positives yields a negative
  or, adding two negatives gives a positive
  or, subtract a negative from a positive gives a negative
  or, subtract a positive from a negative gives a positive
1
1
1
1
0
1
0
1
1
0
0
1
1
1
0
0
1
1
+
7
3
0
1
–6
1
1
0
0
1
0
1
1
+
–4
–5
7
1
0
Notes: For lecture
Recalled from some earlier slides that the biggest positive number you can represent using 4-bit is 7 and the smallest negative you can represent is negative 8.
So any time your addition results in a number bigger than 7 or less than negative 8, you have an overflow.
Keep in mind is that whenever you try to add two numbers together that have different signs, that is adding a negative number to a positive number, overflow can NOT occur.
Overflow occurs when you to add two positive numbers together and the sum has a negative sign. Or, when you try to add negative numbers together and the sum has a positive sign.
If you spend some time, you can convince yourself that If the Carry into the most significant bit is NOT the same as the Carry coming out of the MSB, you have a overflow.

## Slide 12: Summarizing: MIPS Overflow detection
no overflow is detected when using
  addu, addiu, subu, multu, divu, sltiu, sltu
Operation | Operand A | Operand B | Result indicating overflow
A + B |  0 |  0 | < 0
A + B | < 0 | < 0 |  0
A – B |  0 | < 0 | < 0
A – B | < 0 |  0 |  0

## Slide 13: Dealing with Overflow
Some languages (e.g., C) ignore overflow
  Use MIPS addu, addui, subu instructions to ignore overflow
Other languages (e.g., Ada, Fortran) require raising an exception
  Use MIPS add, addi, sub instructions to detect overflow
  On overflow, MIPS invokes the exception handler
    Save PC in Exception Program Counter (EPC) register
    Jump to predefined handler address
    mfc0 (move from system control) instruction copies EPC value to a general-purpose register to return to the offending instruction after corrective action

## Slide 14: Arithmetic for Multimedia
Graphics and media processing operates on vectors of 8-bit (ex. colors) and 16-bit data (ex. sounds)
  Many graphics and audio applications perform the same operation on vectors of media data
  SIMD (single-instruction, multiple-data)
  Use 64-bit adder, with partitioned carry chain
    Operate simultaneous operations on 8×8-bit, or 4×16-bit, or 2×32-bit vectors
Saturating operations
  On overflow, result is set to the largest representable value (most negative or most positive)
    c.f. 2s-complement modulo arithmetic
  E.g. a volume knob with saturation stops at the highest volume no matter how far you turn it.

## Slide 15: Review: A Full Adder
1-bit Full Adder
A
B
S
carry_in
carry_out
S = A  B  carry_in (odd parity-function)
carry_out = A&B | A&carry_in | B&carry_in
(majority function)
How can we use it to build a 32-bit adder?
How can we modify it easily to build an adder/subtractor?
A | B | carry_in | carry_out | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 16: A 32-bit Ripple Carry Adder/Subtractor
Remember 2’s complement is just
  complement all the bits (xor)
  add a 1 in the least significant bit
1-bit FA
S0
c0=carry_in
c1
1-bit FA
S1
c2
1-bit FA
S2
c3
c32=carry_out
1-bit FA
S31
c31
. . .
A0
A1
A2
A31
B0
B1
B2
B31
add/sub
B0
control
(0=add,1=sub)
B0 if control = 0, !B0 if control = 1
A 0111  0111 B - 0110  +
0001
1001
1
1 0001
Notes: The xor complements each bit of B
  C0 = 1 since we must add 1 to B to obtain the 2s’ complement.
  So first step we add a0 + b0 + c0 then we proceed with the rest of the addition.

## Slide 17: Multiply
Binary multiplication is just a bunch of right shifts and adds
multiplicand
multiplier
partial
product
array
double precision product
n
2n
n
can be formed in parallel and added in parallel for faster multiplication

## Slide 18: Multiplication Hardware
Initially 0

## Slide 19: Multiplication
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication
Initially 0

## Slide 20: Optimized Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low

## Slide 21: Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel

## Slide 22: MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
Signed Multiplication
    Convert Multiplicand and Multiplier to positive and remember the original signs. Product is negative if the original signs disagree.

## Slide 23: Next Lecture and Reminders
Next lecture
  Improving Multiplication
  Addressing Division and Floating Point
    Reading assignment – PH, Chapter 3, 3.4-3.6 and 3.8